## Slide 1: Contribution of Wintertime Wood Smoke to Nonattainment Areas in California under the Proposed NAAQS
Kasia Turkiewicz
National Residential Wood Smoke Workshop, Denver, April 11-13, 2023

## Slide 2: Presentation Overview
PM2.5 Monitoring Requirements
Portola PM2.5 Case Study
Impact of Proposed PM2.5 NAAQS in California
Home Heating

## Slide 3: PM2.5 Monitoring Requirements
Number of required monitors depends on population and PM2.5 levels
PM2.5 monitors are not required in low-population areas
Many communities with wood smoke problem may not have regulatory PM2.5 monitors
MSA Population | Design Value >=85% NAAQS | Design Value <85% NAAQS
> 1,000,000 | 3 | 2
500,000 - 1,000,000 | 2 | 1
50,000 - < 500,000 | 1 | 0

## Slide 4: PM2.5 Monitoring Network in the US

## Slide 5: PM2.5 Monitoring Sites in California

## Slide 6: Nature of PM2.5 Pollution Across California
Regional variability influenced by climate, socioeconomic factors, and local regulations and incentives
Mountains
Central CA
Southern CA
Notes: At the end of this slide pivot to say that now I am going to focus on Portola PM2.5 nonattainment area.

## Slide 7: Portola PM2.5 case study

## Slide 8: Nature of PM2.5 Problem in Portola
Mountain valley
No access to natural gas
Potential loss of electricity during storms
Easy access to free or inexpensive wood
Limited income
Chart: Correlation between Levoglucosan and PM2.5 Mass

## Slide 9: Portola Home Heating Landscape
Households by Heating Fuel
Chart: 
| Wood - Primary | Wood - Secondary | Non-wood heating
Number of Households | 822 | 444 | 956
Devices Subject to Change-out
Chart: Number of Devices
| Changed-out | Remaining
Uncertified | 446 | 265
Fireplaces | 60 | 79

## Slide 10: Portola Percent Composition
2018-2021 Annual Average
2017-2022 Exceedance Day
Chart: 
| Ammonium Nitrate | Ammonium Sulfate | Organic Matter | EC | Geological | Elements
 | 0.3707 | 0.4635 | 10.1282 | 1.0444 | 0.70797 | 0.24356
Chart: 
| Ammonium Nitrate | Ammonium Sulfate | Organic Matter | EC | Geological | Elements
 | 1.2185 | 0.62134 | 37.1162 | 3.3917 | 0.44909 | 0.51154

## Slide 11: Portola Annual Average Composition
Chart: PM2.5 Concentrations (ug/m3)
| 2017 | 2018 | 2019 | 2020/2021
Geological | 0.49053 | 0.81598 | 0.55463 | 0.75329
Elements | 0.24366 | 0.2605 | 0.22357 | 0.2466
Ammonium Nitrate | 0.45078 | 0.44997 | 0.30487 | 0.35727
Ammonium Sulfate | 0.58606 | 0.49596 | 0.38819 | 0.50636
EC | 1.171 | 1.2296 | 1.0112 | 0.89221
Organic Matter | 11.9833 | 11.1398 | 9.6125 | 9.6323
Notes: When it comes to home heating, the activity during covid pandemic increased due to people working and studying from home and the need to keep that home warm during the day.

## Slide 12: Portola PM2.5 Seasonality
Chart: Month
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Geological | 0.36041 | 0.67444 | 0.42177 | 0.86922 | 1.014 | 0.7821 | 0.8948 | 0.66017 | 0.59734 | 0.60308 | 0.48795 | 0.31019
Elements | 0.3465 | 0.33335 | 0.26581 | 0.2321 | 0.17307 | 0.19113 | 0.18197 | 0.17297 | 0.21293 | 0.21512 | 0.2715 | 0.32252
Ammonium Nitrate | 0.72428 | 0.44806 | 0.42775 | 0.35831 | 0.21942 | 0.22446 | 0.24645 | 0.26772 | 0.23951 | 0.29796 | 0.39796 | 0.79586
Ammonium Sulfate | 0.35359 | 0.30321 | 0.37098 | 0.62985 | 0.48583 | 0.60037 | 0.7688 | 0.72864 | 0.53038 | 0.42525 | 0.36647 | 0.36907
EC | 2.155 | 1.6956 | 1.5882 | 0.89476 | 0.43591 | 0.22326 | 0.2657 | 0.21 | 0.46056 | 1.21 | 1.6489 | 2.0917
Organic Matter | 23.3693 | 16.4732 | 16.549 | 6.9396 | 2.9945 | 2.3681 | 3.8723 | 3.4272 | 5.3037 | 8.8486 | 15.3662 | 20.7885
Notes: From May through September the average monthly low temperatures are above 30, but the rest of the year, they are below 30.

## Slide 13: Impact of Proposed new PM2.5 NAAQS in California

## Slide 14: Potential Nonattainment Areas in California under Different NAAQS Levels
12 (ug/m3) | 11 (ug/m3) | 10 (ug/m3) | 9 (ug/m3) | 8 (ug/m3)
SC | SC | SC | SC | SC
SJV | SJV | SJV | SJV | SJV
Portola | Portola | Portola | Portola | MC
 | GBV | GBV | GBV | GBV
 |  | SS | SS | SS
 |  |  | SD | SD
 |  |  | SFB | SFB
 |  |  | SV | SV
 |  |  |  | MD
 |  |  |  | NC

## Slide 15: Levoglucosan Levels Across the State
Chart: Levoglucosan Concentrations (ug/m3)
| Jan | Feb | March | April | Oct | Nov | Dec
Portola | 2.2482 | 1.4364 | 1.162 | 0.51087 | 0.83733 | 1.5287 | 1.9753
Modesto | 0.30447 | 0.148 | 0.083235 | 0.023947 | 0.061513 | 0.31029 | 0.38427
Visalia | 0.22411 | 0.16074 | 0.08755 | 0.023936 | 0.051733 | 0.254 | 0.36067
Calexico | 0.15944 | 0.060132 | 0.014611 | 0.014467 | 0.014193 | 0.058786 | 0.342
Chico | 0.62471 | 0.28393 | 0.18615 | 0.0309 | 0.09906 | 0.31338 | 0.91733
Sacramento | 0.20019 | 0.1039 | 0.0572 | 0.014863 | 0.094064 | 0.22811 | 0.28941

## Slide 16: 2019-2021 Winter Average Composition
Chart: PM2.5 Concentrations (ug/m3)
| Portola | Los Angeles | Riverside | Bakersfield | Fresno | Modesto | Visalia | Calexico | El Cajon | San Jose | Chico | Sacramento-Del Paso | Sacramento-T
Geological | 0.31608 | 0.34108 | 0.28715 | 0.2919 | 0.29896 | 0.44747 | 0.38124 | 0.77116 | 0.41447 | 0.48775 | 0.35891 | 0.26405 | 0.35099
Elements | 0.52852 | 1.0038 | 1.4207 | 1.1595 | 0.75711 | 0.79476 | 1.0379 | 2.3672 | 0.62059 | 0.60317 | 0.56543 | 0.43176 | 0.77313
Ammonium Nitrate | 0.48521 | 5.2995 | 4.8733 | 9.5733 | 7.468 | 5.7681 | 8.9272 | 2.4172 | 2.8772 | 2.68 | 1.6901 | 3.5666 | 3.6191
Ammonium Sulfate | 0.32578 | 1.0433 | 0.75264 | 1.3956 | 1.1849 | 1.1302 | 1.3894 | 0.76928 | 0.85823 | 0.75993 | 0.55217 | 0.71836 | 0.76435
EC | 1.6839 | 1.4072 | 1.4852 | 1.4347 | 1.5358 | 0.76865 | 0.73886 | 0.92769 | 1.4268 | 1.2467 | 0.65517 | 2.1267 | 0.71316
Organic Matter | 17.6843 | 4.4279 | 4.4464 | 7.9389 | 8.2757 | 6.9935 | 8.0341 | 4.8458 | 5.1226 | 5.1615 | 7.379 | 6.2611 | 6.9832

## Slide 17: Wintertime Percent Composition
Chart: Portola
| Ammonium Nitrate | Ammonium Sulfate | OrganicMatter | EC | Geological | Elements
 | 0.48521 | 0.32578 | 17.6843 | 1.6839 | 0.31608 | 0.52852
Chart: Chico
| Ammonium Nitrate | Ammonium Sulfate | OrganicMatter | EC | Geological | Elements
 | 1.6901 | 0.55217 | 7.379 | 0.65517 | 0.35891 | 0.56543
Chart: Sacramento-Del Paso
| Ammonium Nitrate | Ammonium Sulfate | OrganicMatter | EC | Geological | Elements
 | 3.5666 | 0.71836 | 6.2611 | 2.1267 | 0.26405 | 0.43176

## Slide 18: Home heating

## Slide 19: Future of Home Heating
Ultimate goal - transition to low-carbon fuels
Interim goal - reduce emissions from wood heating through change-out programs
  Statewide - California Climate Investment Woodsmoke Reduction Program
  Local - Funded locally or with U.S. EPA Targeted Airshed Grant funds
  Need U.S. EPA cooperation and support to ensure certified devices reduce emissions

## Slide 20: Woodsmoke Reduction Program
$18 M allocated
$7.8 M implemented
$6.2 M benefiting priority populations
2,260 stoves changed-out
Notes: 28 out of California’s 35 air districts participated in 2018-2019 program

## Slide 21: Summary
PM2.5 monitoring in low population areas impacted by wood smoke is not required
Annual PM2.5 levels in wood-burning communities may be higher than in large metropolitan areas
Wood smoke contributes to PM2.5 nonattainment areas across California and in some areas it’s a sole contributor
Deficiencies in the current U.S. EPA certification program delayed PM2.5 attainment
Robust certification program will be essential for reaching attainment in wood smoke dominated areas
Notes: Woodsmoke contributes to PM2.5 nonattainment areas across California and in some areas it’s a sole contributor. The current framework of the U.S. EPA certification program may have delayed attainment. U.S. EPA U.S. EPA needs to do a better job in ensuring that the reductions in emissions from change-out programs are in line with the emission factors which are factored into attainment modeling.